## Slide 1: StarR3D Qualification Parameter Tuning
Justin Liang
1/20/2020

## Slide 2: Qualification process flow
Checkout and run qualification test suite (from Austin)
If there is outlier, iteratively do :
  Adjust parameters in C++ codes and compile
  Rerun cases
Final qualification check
Checkin code
Run QA (Rapid3D)
Check-in fixing codes
Check Outlier
Adjust code and Compile
Pass Criteria?
New Case
Yes
No
Manual work
Code change

## Slide 3: Report file (StarFS BEOL)
Ct criteria:
StrAB
    MEAN: 0.5%
    2SIGMA: 2%
  Mesh
  MEAN: 0.5%
  2SIGMA: 3%
  Others
  MAX
Category:
Mesh
StrAB_gds
StrAB_lefdef
mesh_gds
mech_lefdef
BEOL
dummy
beol
StarRC: only need to pass the item “all Cap”
StarQTF: need to pass all item

## Slide 4: Rapid3D test pattern
Target Net
Layer: M x
Layer: M x-1
Layer: M x+1
Target Net
x
y
z
Top View
Side View
Metal line width
Spacing
All StrAB patterns can be classified with metal line width and spacing.
Mesh patterns are more complicated.
  Metal line projection length, upper layer, lower layer

## Slide 5: Rapid3D test pattern
StrAB
M1
M2
M3
M2
Mesh
*Upper and lower layers are metal plat and not show here.
*Upper and lower layers are perpendicular metal lines with different pitches.
** The nearby lines can be shorter than the target net metal line. (Projection length <= 100% length of center lines)
200um X 200um
200um X 200um

## Slide 6: Tuning for outlier
Width (Å)
Width (Å)
Spacing (Å)
Ct < golden
Ct >= golden
Each circle stands for Ct error of a pattern. Circle size is proportional to the Ct error.
Ct error = (Ct – CtRef) /CtRef
Pattern number for StrAB: 200 (N16) ~ 2200 (N3)
Ct error (before tuning)
The Ct error highly depends on metal line width and spacing.
Hence, the tuning process is equivalent to create an adjusting function

## Slide 7: Rapid3d code for tuning
Code for Qualification
  Hard coding every qualification rules in C++
Tuning flow
  Add code for new process version
  For specific test patterns
    Add/adjust rule for specific test patterns
      E.g. if width within (w1, w2) and spacing within (sp1, sp2) adjust_width(w_ext1);
    Compile and check again till converged
  Repeat for all category/layers/patterns
wext
z1adj
z0adj
zhiadj
zloadj
If foundry == …
if process == …
if version == …
if layer == …
if width within (w1, w2) and spacing within (sp1, sp2)
adjust_width(w_ext1);
There are 5 parameters used for tuning.
  wext for Ct
  zhiadj, zloadj for decoupling Cc and Ct